## Slide 1: Microsoft Surface Studio
AN INSIDE LOOK AT

## Slide 3: What is Surface Studio?
A desktop PC aimed at creators, to give them all the tools and power they need to practice their craft, as well as perform everyday computing tasks such as email and web browsing, all in one place
Elegant design – a “Floating Sheet of Pixels”, with the thinnest LCD monitor ever built
Transforms the desk into a Studio, allowing the user to be immersively engaged with the touch screen canvas

## Slide 4: Base System
Performance
  CPU: QuadCore i5 or i7 6th Gen Intel Core Processors
  GPU: Nvidia 2GB GTX 965M or 4GB GTX 980M
  Storage: 1TB or 2TB using SSD/HDD Rapid Hybrid Drive
  System Memory: 8GB / 16GB / 32 GB RAM
Features
  4 USB 3.0 ports, mDP, SDXC, GB Ethernet
  Audio Headset Jack
  Kensington Lock Feature
  AC Power Outlet
  Speaker
  Internal PSU: 270W
Compact, low-profile product design
  250 x 220 x 32.2 mm
Graphite Heat Spreader
Hinge Base Brackets
Main PCBA
Thermal Module
Power Supply
Speaker
Fans

## Slide 5: Base Thermal Management
Thermal Module
Heat
Heat
Heat
RADIATOR
RADIATOR
AIR DIRECTOR
Cool Air
Hot Air
GPU
FAN
CPU
FAN
PSU
FAN
HARD
DRIVE
CPU
GPU
PSU
Heat Sources

## Slide 6: Base AC Plug
Custom-designed plug perfectly matches the curved profile of cover
Strain-relief coupler prevents plug from inadvertently disengaging when pulling on the cord alone

## Slide 7: Monitor System
Thin, minimalist design to showcase display quality
  Edge-to-edge glass
  Narrow bezels
  Seamless back cover
Features
  5MP Camera with 1080p Video / IR Camera
  Power and Volume Buttons
  Wi-Fi, BT, Xbox Controller
  Dual Microphones
  Stereo speakers

## Slide 8: Monitor Back Cover
Aluminum back cover with internal steel stiffeners to provide rigidity and distribute loads from the hinge
Complex fabrication process: stamping, forging, CNC, injection molding, assembly

## Slide 9: Hinge System
“Zero Gravity Hinge” supports the Monitor and provides effortless transition between the upright Desktop Mode to the 20° Studio Mode
Chrome hinge arms house linkages that control a fixed path of motion, as well as the cable assemblies for signal and power between the Base and Monitor

## Slide 10: Understanding User Experience
Chart: Position (% Span)

## Slide 11: Hinge Counterbalance Spring System
3 sets of springs work together to counterbalance the ~13 lb Monitor through the full range of motion and enables it to feel near-weightless in any position
4 large compression springs in the base (1) are linked through the arms to one large torsion spring (2) that is always engaged and one small torsion spring (3) engaged only during a portion of the motion to perfect the user experience
3
2
1

## Slide 12: Hinge Arm Linkage
Each hinge arm contains a multi-bar linkage system that translate loads from the top axis to the bottom
The linkage system also sets the path of the Monitor by establishing a relationship between top and bottom rotation

## Slide 13: Hinge Arm Cables
2 high-speed, high-density electrical cables route inside the arms and pass through openings into the Base and Monitor
Cables sweep side to side within the arm during hinge rotation, allowing cable stress to be minimized over the very large range of motion

## Slide 14: Bringing it Together
We obsessed over every detail during design and manufacturing
  Every hinge assembly is custom tuned at the factory with 11 independent adjustments to calibrate for variations in the springs, linkages, Monitor weight and assembly variation
  Precision glass alignment to the Monitor housing is achieved via optical alignment and robotic placement